## Slide 1
April Novak
Assistant Professor
Nuclear, Plasma, and Radiological Engineering (NPRE)
University of Illinois, Urbana-Champaign
Joint Appointment, Nuclear Science and Engineering (NSE) Division
Argonne National Laboratory
Cardinal: Integrating NekRS with the MOOSE Ecosystem

## Slide 2
(Re)-Introduction to Cardinal and NekRS (15 min)
Flow over a pebble, NekRS + MOOSE conjugate heat transfer coupling (75 min)
Notes: complementary to experimental programs

## Slide 3
Objectives:
Introduce how to couple OpenMC to MOOSE
Learn how to apply multiphysics feedback to CAD Monte Carlo models
Explore data postprocessing in Cardinal
Assumptions:
Attended the OpenMC and MOOSE workshop sessions
Basic familiarity with Unix-based environment
Basic familiarity with radiation transport and heat conduction
Notes: complementary to experimental programs

## Slide 4: Cardinal
Couples the NekRS computational fluid dynamics code to MOOSE
Open source, extensible for research purposes
Adopt best practices for software development
High performance, scalable on HPC
Can be used to predict:
  Heat transfer and fluid flow
  Temperature and heat flux thermal limits
  Pressure losses and pumping power
  Passive scalar transport (e.g., mass transport)
  Magnetohydrodynamics
  Fluid-structure interaction
Velocity and temperature in CHIMERA
and how these are influenced by OTHER PHYSICS
Simulations performed by Kirk Yuan (ANL), Tri Nguyen (PSU), Elia Merzari (PSU), and Yu-Hsiang Lan (UIUC)

## Slide 5: NekRS Integration
Turbulence models: DNS, RANS, LES
  DNS flow (including laminar)
  LES flow
  RANS flow
  Fission reactor
  Carolina Bourdot Dutra (PSU)
  Fission reactor
  Yiqi Yu (ANL)
  CHIMERA
Kirk Yuan (ANL), Tri Nguyen (PSU), Elia Merzari (PSU), and Yu-Hsiang Lan (UIUC)

## Slide 6: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification

## Slide 7: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
Conjugate heat transfer in a 67-pebble bed.
Courtesy of David Reger and Elia Merzari (PSU).
NekRS + MOOSE heat transfer module
NekRS
any MOOSE app

## Slide 8: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
NekRS
any MOOSE app
Volume coupling to radiation transport for a molten salt reactor.
NekRS + OpenMC

## Slide 9: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
Fluid-structure interaction for cylinder in crossflow.
Courtesy of David Reger and Elia Merzari (PSU).
NekRS + MOOSE solid mechanics module
NekRS
any MOOSE app

## Slide 10: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
NekRS
any MOOSE app
CFD-systems coupling for tracer mixing in a double-T junction.
Courtesy of Aaron Huxford and Annalisa Manera (ETH).
NekRS + SAM

## Slide 11: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
Forward uncertainty quantification (UQ) for hot channel estimation in fast reactors.
Courtesy of Hansol Park, Yiqi Yu, and Emily Shemon (ANL).
NekRS + MOOSE stochastic tools module

## Slide 12: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
Data transfer: interpolate between NekRS mesh and a MOOSE mesh
Nth order  1st order
Nth order  2nd order
exact replication
Data transfer options in Cardinal
Example of lowest-order data transfer from NekRS (top) onto a MOOSE mesh (bottom)

## Slide 13: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
Data transfer: interpolate between NekRS mesh and a MOOSE mesh
Conservation is ensured by normalizing all quantities.

## Slide 14: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
Data transfer: interpolate between NekRS mesh and a MOOSE mesh
Parallelism: NekRS runs on CPU/GPU, MOOSE runs on CPU

## Slide 15: NekRS Integration
Turbulence models: DNS, RANS, LES
Coupling modes: boundary (conjugate) heat transfer, volume heat generation, fluid-structure interaction, systems-CFD coupling, forward uncertainty quantification
Data transfer: interpolate between NekRS mesh and a MOOSE mesh
Parallelism: NekRS runs on CPU/GPU, MOOSE runs on CPU
Other features: Constitutive model development, averaging onto coarse meshes

## Slide 16: Cardinal
wall temperature
fluid density
fluid temperature
inlet/outlet BCs
tallies (e.g. power, fluence)
NekRS
OpenMC
Write NekRS solution into AuxVariables
Read heat flux, power density, displacement from AuxVariables into NekRS
Allows NekRS to interact with MOOSE for physics feedback and postprocessing

## Slide 17: Cardinal
NekRS
wall heat flux
power density
inlet/outlet BCs
OpenMC
temperature
density
Write OpenMC tallies into AuxVariables
Read temperature, density, displacement from AuxVariables into OpenMC
Allows OpenMC to interact with MOOSE for physics feedback and postprocessing
geometry
composition

## Slide 18: Docker Instructions
To test if Docker works:
cd openmc/live
cardinal-opt -i testing.i

## Slide 19: Compiling Cardinal (After the workshop!)
git clone https://github.com/neams-th-coe/cardinal.git
cd cardinal
./scripts/get-dependencies.sh
./contrib/moose/scripts/update_and_rebuild_petsc.sh ./contrib/moose/scripts/update_and_rebuild_libmesh.sh ./contrib/moose/scripts/update_and_rebuild_wasp.sh
export NEKRS_HOME=$HOME/cardinal/install/bin
make -j8
Compile all dependencies with a single make command, which gives you:
  Cardinal executable (cardinal/cardinal-opt)
  “standalone” OpenMC executable (cardinal/build/openmc/bin/openmc)
  “standalone” NekRS executable (cardinal/install/bin/nrsmpi)
Nek5000 tools (exo2nek) are used to prepare meshes:
git clone https://github.com/Nek5000/Nek5000.git
cd Nek5000/tools
./maketools exo2nek
download the Cardinal source code
download the OpenMC and NekRS
source code
build MOOSE 3rd-party dependencies
set environment variable
compile Cardinal

## Slide 20: How to Get Involved
Git repository:
  Cardinal: https://github.com/neams-th-coe/cardinal
  NekRS: https://github.com/Nek5000/nekRS
Discussions page:
  Cardinal: https://github.com/neams-th-coe/cardinal/discussions
  NekRS: https://github.com/Nek5000/nekRS/discussions
Documentation:
  Cardinal: https://cardinal.cels.anl.gov/
  NekRS: https://nekrsdoc.readthedocs.io
Contact us directly!
  April Novak: ajnovak2@Illinois.edu (Cardinal lead)
  Dillon Shaver: dshaver@anl.gov (Nek lead)

## Slide 21: Example: Flow Over a Pebble
Link: https://cardinal.cels.anl.gov/tutorials/cht5.html
pebble diameter: 3 cm
box dimensions: 5 cm x 5 cm x 43 cm
water fluid
Intro to conjugate heat transfer coupling (75 min)
Objectives:
  How to couple NekRS to MOOSE for conjugate heat transfer
  How to visualize output files

## Slide 22: NekRS Input Files
<case>.re2: mesh (Hex8 or Hex20)
<case>.par: high-level settings for the equations, time stepping, I/O, …
<case>.oudf: OKL-language “kernels” that run on “backend” (e.g. GPU)
  boundary conditions
  any other user-specified physics
<case>udf: C++ user interaction which runs on the “host” (e.g. CPU)
  initial conditions
  postprocessing
  pass stuff between device (GPU) and host (CPU)
Optional:
  <case>.usr: Fortran backend to access Nek5000 features
A note on naming conventions:
  o_name and name hold the same data, but o_name is on the device (GPU) whereas name is on the host (CPU)

## Slide 23: Geometry: pebble.exo, pebble.re2
Mesh must be 3-D
Sidesets must be numbered consecutively, beginning from 1
  1: inlet
  2: outlet
  3: pebble surface
  4: walls
The mesh Nek uses internally
The mesh you create

## Slide 24: Parameter settings: pebble.par
High-level settings for solver, boundary conditions, and equations to solve

## Slide 25: Kernels and boundary conditions: pebble.oudf
Boundary conditions are specified using kernels connected to the choices made in the .par file
The only difference now is that we are not going to hand-write the heat flux value – it’s going to come from MOOSE!

## Slide 26: Initial conditions and user interfaces: pebble.udf
UDF_LoadKernels will load any user-defined physics kernels
UDF_Setup is called on initialization, typically where initial conditions are applied
UDF_ExecuteStep is called each time step, typically where postprocessing is applied
Commonly-used variables: https://nekrsdoc.readthedocs.io/en/latest/commonly_used_variables.html

## Slide 27: Legacy backend: pebble.usr
Fortran file to perform custom user actions - will eventually be deprecated, but still widely used to streamline porting from Nek5000 to NekRS

## Slide 28: Solid heat conduction: solid.i

## Slide 29: Multiphysics Coupling
Repeat until convergence:
  Run MOOSE.
  Send to NekRS as a boundary condition.
  Run NekRS.
  Send to MOOSE as a boundary condition.
  Is the simulation converged?

## Slide 30: MultiApps and Transfers

## Slide 31: Sub-cycling
MOOSE MultiApps can use “subcycling”
  Each application can use its own time steps
  Synchronization (i.e. data transfers) according to the parent app’s time stepping
Parent application
0
1
2
5
3
4
0
Child application
0.2
0.6
1.1
1.7
3.6
2.6
4.6

## Slide 32: Sub-cycling
MOOSE MultiApps can use “subcycling”
  Each application can use its own time steps
  Synchronization (i.e. data transfers) according to the parent app’s time stepping
Parent application
0
1
2
5
3
4
0
Child application
0.2
0.6
1.1
1.7
3.6
2.6
4.6
1.0
2.0
4.0
3.0
5.0

## Slide 33: Coupled Model: solid.i, nek.i

## Slide 34: Calculate a Heat Transfer Coefficient

## Slide 35
Cardinal couples NekRS to MOOSE for multiphysics feedback and data postprocessing
Additional tutorials which couple NekRS to MOOSE: https://cardinal.cels.anl.gov/tutorials/index.html