## Slide 1
April Novak
Assistant Professor
Nuclear, Plasma, and Radiological Engineering (NPRE)
University of Illinois, Urbana-Champaign
Joint Appointment, Nuclear Science and Engineering (NSE) Division
Argonne National Laboratory
Cardinal: Integrating OpenMC with the
MOOSE Ecosystem

## Slide 2
(Re)-Introduction to Cardinal and OpenMC (15 min)
Tokamak, OpenMC + heat conduction coupling (75 min)
Notes: complementary to experimental programs

## Slide 3
Objectives:
Introduce how to couple OpenMC to MOOSE
Learn how to apply multiphysics feedback to CAD Monte Carlo models
Explore data postprocessing in Cardinal
Assumptions:
Attended the OpenMC and MOOSE workshop sessions
Basic familiarity with Unix-based environment
Basic familiarity with radiation transport and heat conduction
Notes: complementary to experimental programs

## Slide 4: Cardinal
Couples the OpenMC Monte Carlo neutron and photon transport code to MOOSE
Open source, extensible for research purposes
Adopt best practices for software development
High performance, scalable on HPC
Can be used to predict:
  Tritium breeding
  Nuclear heating (power deposition)
  Shielding requirements
  Material activation, radioactive waste classification
  Material damage (DPA), gas production
  Non-proliferation analyses
  Diagnostics, sensor responses
Tritium production in a breeder module
and how these are influenced by OTHER PHYSICS
Notes: complementary to experimental programs

## Slide 5: OpenMC
Modes/solvers: Fixed-source, k-eigenvalue, depletion, volume, geometry plotting
  Fixed source neutron-photon transport
  built-in geometry plotter
  k-eigenvalue neutron transport
  Breeder blanket module
  Fission reactor
  Fission test reactor
Notes: complementary to experimental programs

## Slide 6: OpenMC
Modes/solvers: Fixed-source, k-eigenvalue, depletion, volume, geometry plotting
Geometry: Constructive solid geometry, CAD surface mesh, unstructured mesh
  Constructive Solid Geometry (CSG)
  DAGMC CAD surface meshes
  libMesh unstructured volume mesh
Notes: complementary to experimental programs

## Slide 7: OpenMC
Modes/solvers: Fixed-source, k-eigenvalue, depletion, volume, geometry plotting
Geometry: Constructive solid geometry, CAD surface mesh, unstructured mesh
Tallies: cell tallies, structured mesh tallies, unstructured mesh tallies
  Cell tally
  Structured mesh tally
  Unstructured mesh tally
Notes: complementary to experimental programs

## Slide 8: OpenMC
Modes/solvers: Fixed-source, k-eigenvalue, depletion, volume, geometry plotting
Geometry: Constructive solid geometry, CAD surface mesh, unstructured mesh
Tallies: cell tallies, structured mesh tallies, unstructured mesh tallies
Data: Continuous energy or multigroup , multipole for Doppler broadening
Notes: complementary to experimental programs

## Slide 9: OpenMC
Modes/solvers: Fixed-source, k-eigenvalue, depletion, volume, geometry plotting
Geometry: Constructive solid geometry, CAD surface mesh, unstructured mesh
Tallies: cell tallies, structured mesh tallies, unstructured mesh tallies
Data: Continuous energy or multigroup , multipole for Doppler broadening
Parallelism: hybrid MPI and OpenMP
Notes: complementary to experimental programs

## Slide 10: Cardinal
wall temperature
fluid density
fluid temperature
inlet/outlet BCs
tallies (e.g. power, fluence)
NekRS
OpenMC
Write OpenMC tallies into AuxVariables
Read temperature, density, displacement from AuxVariables into OpenMC
Allows OpenMC to interact with MOOSE for physics feedback and postprocessing

## Slide 11: Cardinal
NekRS
wall heat flux
power density
inlet/outlet BCs
OpenMC
temperature
density
Write OpenMC tallies into AuxVariables
Read temperature, density, displacement from AuxVariables into OpenMC
Allows OpenMC to interact with MOOSE for physics feedback and postprocessing
geometry
composition

## Slide 12: Docker Instructions
To test if Docker works:
cd openmc/live
cardinal-opt -i testing.i
Notes: complementary to experimental programs

## Slide 13: Compiling Cardinal (After the workshop!)
git clone https://github.com/neams-th-coe/cardinal.git
cd cardinal
./scripts/get-dependencies.sh
./contrib/moose/scripts/update_and_rebuild_petsc.sh ./contrib/moose/scripts/update_and_rebuild_libmesh.sh ./contrib/moose/scripts/update_and_rebuild_wasp.sh
make -j8
Compile all dependencies with a single make command, which gives you:
  Cardinal executable (cardinal/cardinal-opt)
  “standalone” OpenMC executable (cardinal/build/openmc/bin/openmc)
  “standalone” NekRS executable (cardinal/install/bin/nrsmpi)
Can selectively enable parts of Cardinal using ENABLE_NEK, ENABLE_OPENMC, ENABLE_DAGMC
General workflow:
  Develop ”standalone” NekRS/OpenMC input files
  Develop a MOOSE-type “wrapper” input file
  Ready to run!
download the Cardinal source code
download the OpenMC and NekRS
source code
build MOOSE 3rd-party dependencies
compile Cardinal

## Slide 14: How to Get Involved
Git repository: https://github.com/neams-th-coe/cardinal
Discussions page: https://github.com/neams-th-coe/cardinal/discussions
Documentation: https://cardinal.cels.anl.gov/
Contact us directly!
  April Novak: ajnovak2@Illinois.edu (Cardinal lead)
  Paul Romano: promano@anl.gov (OpenMC lead)
  Dillon Shaver: dshaver@anl.gov (Nek lead)

## Slide 15: Example: Tokamak
Link: https://cardinal.cels.anl.gov/tutorials/tokamak.html
Objectives:
  How to generate a CAD Monte Carlo geometry
  How to set up Cardinal input files for coupling OpenMC with heat conduction
  How to visualize Cardinal output files
Input files:
  Meshes
  MOOSE heat conduction solve: solid.i
  “Standalone” OpenMC solve: model.py
  Cardinal wrapping solve: openmc.i

## Slide 16: Geometry
Section of a tokamak built using CAD.
Facet the surfaces.
Volume unstructured mesh: heat conduction, tallying in OpenMC, and reading/writing multiphysics data in/out of OpenMC
Surface unstructured mesh: to enclose cells for Monte Carlo transport
Mesh the volume to give the
VOLUME MESH
Export just the surfaces to get the
SURFACE MESH

## Slide 17: Geometry: tokamak.jou

## Slide 18: Geometry: tokamak.jou
import STEP file  prepare geometry  mesh  export

## Slide 19: Geometry: tokamak.jou
import STEP file  prepare geometry  mesh  export

## Slide 20: Geometry: tokamak.jou
import STEP file  prepare geometry  mesh  export
sweep into 3D

## Slide 21: Geometry: tokamak.jou
import STEP file  prepare geometry  mesh  export
Create material tags and assign to blocks (this is how we tell OpenMC where to place material compositions):
create material 'ss316' property_group 'CUBIT-ABAQUS’
block 5 material 'ss316'

## Slide 22: Geometry: tokamak.jou
import STEP file  prepare geometry  mesh  export
Volume mesh
Add a graveyard, then export surface mesh

## Slide 23: MOOSE Heat Conduction Model: solid_standalone.i
Mesh
Governing equation (cooling is approximated by a volumetric heat sink)
Boundary conditions
Initial conditions
Material properties

## Slide 24: OpenMC Standalone Model: model.py, openmc_standalone.i
Create XML files from model.py
  Can run this just like you run a normal OpenMC model
Create a thin “wrapping” file with openmc_standalone.i
  Maps data in/out of OpenMC into MOOSE AuxVariables

## Slide 25: Multiphysics Coupling
Repeat until convergence:
  Run MOOSE.
  Send to OpenMC cells in order to update cross sections.
  Run OpenMC
  Send to MOOSE as a volumetric heat source.
  Is the simulation converged?

## Slide 26: MultiApps and Transfers

## Slide 27: Geometry Skinning
OpenMC can only use a single temperature/density for every cell (5 temperatures in this case!)
On-the-fly geometry refinement to resolve temperature, density fields (developed by Dr. Helen Brooks, UKAEA)

## Slide 28: Coupled Model: openmc.i, solid.i

## Slide 29
Cardinal couples OpenMC to MOOSE for multiphysics feedback and data postprocessing
Additional tutorials which couple OpenMC to MOOSE: https://cardinal.cels.anl.gov/tutorials/index.html
Notes: complementary to experimental programs